## Slide 1: Session Four

## Slide 2: How do FPGA do Math?

## Slide 3: Why do we need to do math in FPGA
Programmable Logic enables accelerated applications
Image Processing – Noise removal, edge detection, filtering
Radar Processing – Signal generation, reply processing
Signal Processing – Signal filtering & manipulation
Robotics – End Effector positioning, Navigation
Control Systems – Kalman Filtering, PID Loops
Motor Control – Servo Motor, DC Motor Control
All these applications require the ability of FPGA to do Maths and implement algorithms.

## Slide 4: Example applications
Background Removal & Substitution
Fractals
AI/ML
Edge Detection
Signal Processing

## Slide 5: FPGA Architecture
FPGA are register and logic rich
Configurable Logic Blocks contain
  Registers
  Look Up Table
  Distributed RAM
  Carry Mux
Logic resources are the basic building blocks of our algorithms. It is where we implement our mathematical algorithms

## Slide 6: DSP Elements
Implementing math directly in logic is costly
  Resources – increased resources
  Performance – reduced performance
Manufactures to address this include dedicated DSP elements e.g. DSP48
Capable of doing 48 bit Multiply accumulator
Pre-Adder
Multiply
Accumulator
Can do advance things SIMD – More later!

## Slide 7: FPGA Math's
So far, we have looked at Logic & DSP elements, but they all have one thing in common ?
They are all ideal for the implementation of fixed-point solutions.
What is the difference between fixed point and floating-point numbers ?

## Slide 8: Fixed Point Number
Fixed-point representation maintains the decimal point within a fixed position allowing for straight forward arithmetic operations.
The major drawback of fixed-point representation is that to represent larger numbers or to achieve a more accurate result with fractional numbers, a larger number of bits are required.
A fixed-point number consists of two parts called the integer and fractional parts.
But in programmable logic Fixed Point Maths can be very fast

## Slide 9: Floating Point Number
Floating point representation allows the decimal point to float to different places within the number depending upon the magnitude.
The floating-point number is standardized by an IEEE / ANSI Standard 754-1985 the basic IEEE floating point number

## Slide 10: Why Fixed Point
Less complex to implement in logic
Enables a faster solution
Can be more power efficient
FPGA are register rich!
No standard for implementation but, Q format is popular
  Q15 – 15 fractional bits
  M,N – M integer bits and N fractional bits

## Slide 11: Number schemes
Fixed point numbers need to represent positive and negative numbers
Sign and Magnitude - Utilises the left most bit to represent the sign of the number (0 = positive, 1 = negative) the remainder of the bits represent the magnitude. BUT! Positive and Negative Numbers
Ones Complement – Same unsigned representation for positive numbers as Sign and Magnitude representation. However, for negative numbers the inversion (ones complement) of the positive number are used. Requires end around carry for subtraction – Added complexity.
Twos Complement – Positive are represented in the same manner as an unsigned numbers. While negative numbers are represented as the binary number you add to a positive number of the same magnitude to get zero

## Slide 12: Twos Compliment
A negative twos complement number is calculated by first taking the ones complement (inversion) of the positive number and then adding one to it. The twos complement number system allows subtraction of one number form another by performing an addition of the two numbers. The range a twos complement number can represent is given by
(2n-1) to + (2n-1 – 1)
One method we can use to convert a number to its twos complement format is to work right to left leaving the number the same until the first one is encountered, after this each bit is inverted.

## Slide 13: Fixed Point
How many bits do we need to represent my value ?
For example, the number of integer bits required to represent a value between 0.0 and 423.0

## Slide 14: Fixed Point
How do we work out fractional bit ? Trade off between bit length and accuracy
To store the number 1.45309806319x10-4
Multiply by 2^16 1.45309806319x10-4 * 65536 = 9.523023
Can only store 9 in the FPGA registers.
9/65536 = 1.37329101563x10-4
Significant loss of accuracy, how can we address this?

## Slide 15: Fixed Point
We can obtain a more accurate result by scaling the number up by a factor of 2 that produces a result of between 32768 and 65535 therefore still allowing storage in a 16-bit number
268435456 * 1.45309806319x10-4 = 39006.3041205
Stored number therefore 1.45308673382x10-4 (39006/ 268435456)
Number is formatted as Q28 or 1,28

## Slide 16: Fixed Point Rules
Fixed Point Arithmetic does have some rules which must be followed.
Addition - Decimal points must be aligned
Subtraction – Decimal points must be aligned
Division – Decimal Points must be aligned
Multiplication – Decimal points do not need to be aligned

## Slide 17: Fixed Point Result Sizes
Operation | 
A + B | Max(A’left, B’left) + 1 downto Min (A’right, B’right)
A - B | Max(A’left, B’left) + 1 downto Min (A’right, B’right)
A * B | (A’left + B’left) + 1 downto A’right + B’right
A / B - Unsigned | A’left - B’left downto (A’right + B’right) -1
A / B - Signed | (A’left - B’left) +1 downto A’right + B’right

## Slide 18: Implementing in VHDL
Two options
Numeric Standard (pre VHDL 2008)
  Unsigned
  Signed
  Need to keep track of decimal point – Range of number from X downto 0
  Quantisation needs to be performed by developer
  No in-built checking, requires design to check correct sizing / overflow etc
Fixed Point (VHDL 2008)
  Ufixed
  Sfixed
  Decimal point located between the 0 and -1 bit
  Inbuilt checking to ensure correct sizing of results

## Slide 19: Fixed Package
Integer bits are represented in the range MSB down to 0
Fractional bits are represented in the range -1 down to LSB
SIGNAL example : ufixed(3 DOWNTO -3);
Which represents the vector of 000.000 allowing for a range of 0.0 to 7.875
To help initialise signals, variables and constants in our algorithm we can use the to_ufixed and to_sfixed, these can be used with integers, real, ufixed, sfixed and std_logic_vectors.

## Slide 20: What about more complex math
How would I implement the following functions
Sine / Cosine / ArcTan
SineH / CosH / ArcTanH
Square Root
Exponential
Ln
Taylor / Maclaurin Series? Look Up Table ?
But how do we achieve performance ?

## Slide 21: CORDIC Algorithm
CORDIC (COordinate Rotation DIgital Computer) algorithm invented by Jack Volder for B58 Program
Deployed in first scientific calculator HP35
Shift and Add algorithm which can be used to implement transcendental functions.
No dedicated Multiplier required.

## Slide 22: CORDIC Algorithm
Three configurations - Linear / Hyperbolic / Circular
Each mode has two modes – Rotation / Vectoring
Enable a range of complex math's functions to be implemented.
Additional Functions
Tan = Sin / Cos
TanH = Sinh / Cosh
Exponential = Sinh + Cosh
Natural Logarithm = 2 * ArcTanH note 1
SQR = (X2 – Y2)0.5

## Slide 23: More Complex Algorithm
How would you implement the following algorithm
Typical Platinum Resistance Thermometer conversion equation used in industrial applications

## Slide 24: More Complex Algorithm
Chart: Temperature vs Resistance

## Slide 25: Polynomial Approximation
Chart: Temperature vs Resistance

## Slide 26: Polynomial Approximation
Leverage FPGA DSP rich environment – Addition and Multiplication easy to do in FPGA especially as we now know how!
If Accuracy is difficult with one overall polynomial equation – Segment it to several elements
Uniform segmentation
Non-uniform segmentation

## Slide 27: What about signal processing
Finite Impulse Response Filters – Leverage the Multiple Accumulate Capability
Assume an ideal filter in the frequency domain – Brick Wall

## Slide 28: FIR Filter
IFFT of the brick wall filter gives us the Windowed Sync Pulse
The ripples extend to infinity and never settle to zero.

## Slide 29: FIR Filter
Truncating the impulse response gives us ripples – Windowing helps address this

## Slide 30: FIR Filter
Filter Response is improved with window

## Slide 31: FIR Filter
When Implemented (Input top / Output bottom)

## Slide 32: What is PYNQ – Introduction to PYNQ framework

## Slide 33: What is PYNQ?
PYNQ is an open source project started by Xilinx, which fuses the productivity of Python with the acceleration provided by programmable logic within the Zynq / Zynq MPSoC
Hosted at PYNQ.io

## Slide 34: Why should I learn PYNQ ?
Tight coupling of processing system (PS) and programmable logic (PL) in the Zynq / Zynq MPSoC creates a system which is
  Responsive – Leverage the parallel processing capability provided by the PL
  Deterministic – Creates processing pipeline competing for fewer shared resources
  Power Efficient – Less off chip transactions to or from DDR memory, dedicated hardware implementation is more efficient than
PYNQ frees Python programmers from the sequential software world and opens up the acceleration of programmable logic without the need to be a digital designer.

## Slide 35: Why should I learn PYNQ ?
Simple example of PYNQ in a image processing application
  Image Filtering
    SW < 20 Frames per Second
    HW > 60 Frames per Second
  Optical Flow
    SW < 1 Frame per Second
    HW > 120 Frames per Second

## Slide 36: PYNQ Framework: interfacing Python with Xilinx SoC

## Slide 37: PYNQ Components
To achieve performance PYNQ is comprised of
  Jupyter Notebooks
  PYNQ Package
  PYNQ Libs
  PYNQ Classes
  PYNQ IP
  PYNQ Overlays

## Slide 38: PYNQ Architecture
Pynq is built upon Xilinx Petalinux flow
Standard way to create PYNQ for a custom board is via petalinux BSP as we will see

## Slide 39: Working with the PL
Bitstream — This configures the programmable logic for the desired application. In the PYNQ framework, the xdevcfg driver is used.
GPIO — This provides simple IO in both directions. In the PYNQ framework, this is supported by the sysgpio driver.
Interrupts — Support interrupt generation from the programmable logic to the processing system. In the PYNQ framework, this is supported by the Userspace IO driver.
Master AXI Interfaces — These are used to transfer data between the PS to the PL when the PS is the initiator of the transaction. The PYNQ framework uses devmem when employing master AXI interface.
Slave AXI Interfaces — These are used to transfer data between the PS and PL when the PL is the initiator of the transaction. The PYNQ framework uses xlnk to enable these transfers.

## Slide 40: Available PYNQ boards
Several PYNQ builds for existing boards:
  Pynq Z1 — Zynq SoC 7020 & Arty Z7-20
  Pynq Z2 — Zynq SoC 7020
  ZCU104 — Zynq MPSoC XCZU7EV
  ZCU111 — Zynq RFSoC XCZU28DR
  Ultra96 — Zynq MPSoC ZU3EG

## Slide 41: Overlays
Overlays are the design loaded into the programmable logic
Can be custom created or accessed via the PYNQ.IO community
Range of Overlays in the community including
  Machine Learning
  Image Processing
  RISC-V
  Kalman filter
Base Overlay is the initial overlay which is created with the PYNQ Image
Download and work with new overlays as required
Of course you can also create you own – As we will see

## Slide 42: PYNQ Libraries
PYNQ provides several libraries which provide support for management of the processor and allow access to the low level hardware including
IP Cores – Audio, AXI GPIO, AXI IIC, DMA, Logic Tools, Video
IOP – Arduino, Grove, RPI, PMOD
PYNQ MicroBlaze – MicroBlaze Subsystem RPC and Library
PS / PL Interface – Interrupt, MMIO, PS GPIO, Xlnk
PS Control – PMBus
PL Control – Overlay, PL and Bitstream Classes

## Slide 43: PYNQ In Industry
Working with THALES – Major Defense Client – High Speed Image processing (3000 > 10,000 FPS)
ZCU102 Development board
“The use of Pynq to rapidly test and evaluate design patterns for image processing has been invaluable. Not only has it sped up design, but it also reduces the necessary team size to a manageable level.”

## Slide 44
Vitis AI

## Slide 45: Vitis AI Development Environment
Vitis AI enables acceleration of AI inference at edge & Cloud
Supports leading frameworks such as TensorFlow, Caffe and Pytorch
Works with fixed point representation and Xilinx Deep Learning Processor Unit

## Slide 46: Deep Learning Processing Unit
Deep Learning Processing Unit (DPU) is a programmable engine optimized for convolutional neural networks
Can be used to implement
VGG, ResNet, GoogLeNet, YOLO, SSD, MobileNet, and FPN

## Slide 47: DPU Development flow
Use Vitis / Vivado to generate bit stream
Vitis AI to generate the neural network.
Can come from Xilinx Model Zoo

## Slide 48: Example Application
AI is only a small part (but important part) of the solution
Need to be able to get image into or out of the system.
For example, MIPI camera interface

## Slide 49: Clocking the DPU
s_axi_aclk is used for the register configuration module. This module receives the DPU configuration though the S_AXI interface. The S_AXI clock can be configured as common with the M-AXI clock or as an independent clock.
The primary function of the data controller module is to schedule the data flow in the DPU IP. The data controller module works with m_axi_dpu_aclk. The data transfer between the DPU and external memory happens in the data controller clock domain, so m_axi_dpu_aclk is also the AXI clock for the AXI_MM master interface in the DPU IP
The DSP slices in the computation unit module are in the dpu_2x_clk domain, which runs at twice the clock frequency of the data controller module. The two related clocks must be edge-aligned.

## Slide 50: DPU is configurable
Depending on flow either IP integrator or in script (Vitis)
Can control performance and resource usage
Can be deployed in

## Slide 51: Performance Optimisation

## Slide 52: Resource Optimization

## Slide 53: Model Zoo
Networks and many others are often made available for different frameworks in a Model Zoo

## Slide 54: Model Zoo

## Slide 55: Vitis AI Optimizer
Optimizes the network
Reduce model complexity by 5x to 50x with minimal accuracy degradation
Requires a commercial license

## Slide 56: Vitis AI Quantizer
Converts the 32-bit floating-point weights and activations to fixed-point e.g. INT8
Fixedpoint network model requires less memory bandwidth, thus providing faster speed and higher power efficiency than the floating-point mode

## Slide 57: Vitis AI Compiler
Maps the AI model to the instruction set and dataflow model
Performs optimizations such as
  layer fusion,
  instruction scheduling
  reuses on-chip memory.

## Slide 58: Putting it all Together

## Slide 59
www.adiuvoengineering.com
adam@adiuvoengineering.com